Private Drainage Facilities within City Right-of-Way

Notice to Contractor

(Special Order 19 ~  “SO-19”)

- An excavation permit will be required before beginning any work within City Right-Of-Way.

- All work on this project shall be performed in accordance with applicable federal, state and local laws, rules and regulations concerning construction safety and health.

- Two working days prior to any excavation, the contractor must contact New Mexico One Call, dial “811” [or (505) 260-1990] for the location of existing utilities.

- Prior to construction, the contractor shall excavate and verify the locations of all obstructions. Should a conflict exist, the contractor shall notify the engineer so that the conflict can be resolved with a minimum amount of delay.

- Backfill compaction shall be according to traffic/street use.

- Maintenance of the facility shall be the responsibility of the owner of the property being served.

- Work on arterial streets may be required on a 24-hour basis.

- Contractor must contact Jason Rodriguez at 235-8016 and Construction Coordination at 924-3416 to schedule an inspection.