## Slide 1: Integrated Development Ordinance
UNM SAAP
October 2024
Site Plans
https://abq-zone.com
IDO as of August 2024
Michael Vos
Principal Planner
mvos@cabq.gov

## Slide 2: Planning + Zoning
ABC Comprehensive Plan
What we want + why:
  Where to direct growth
  What to protect
  What actions to take
  How to measure progress
Integrated development ordinance
Vision
Regulations
Centers
&
Corridors
Areas of Change
&
Consistency
How to get there:
  Tailored rules
    Centers + Corridors
    Areas of Consistency
    Overlay Zones
    Special places
  Transitions / Edge Protections
    Between Areas of Change + Consistency
    Next to neighborhoods
Policies
compplan.abq-zone.com
https://abq-zone.com
Notes: The WHY and the HOW

## Slide 3: Finding the balance
Incentivizing
High-quality development
in appropriate areas
Protecting
Neighborhoods, special places,
& City open space

## Slide 4: Finding the balance
Citywide
Standardized rules
Tailored
Rules for small areas
Additional complexity
Harder to enforce
Less complexity
Easier to enforce

## Slide 5
structure
Processes
Zones
Uses
Standards
1. General Provisions
Zone Districts
Overlay Zones
4. Use Regulations
Allowable Use Table
Use-specific Standards
Development Standards
      Dimensional Standards Tables
      General Regulations
6. Administration & Enforcement
7. Definitions & Acronyms
IDO Zoning Map
https://tinyurl.com/IDOzoningmap
https://abq-zone.com

## Slide 6
Due Diligence
Processes
Zones
Uses
Standards
What’s the zoning on this property?
Is it in an overlay zone?
What use or uses will be on this property?
Is the use allowed in this zone?
In this area? Any special regs?
What are the development standards?
      In this zone?
      In this area? Any special regs?
What is the review/decision process?
In this area? Any special procedures?
IDO Zoning Map
https://tinyurl.com/IDOzoningmap
Part 2/3
Part 4
Part 5
Part 6
https://abq-zone.com

## Slide 7: Levers for regulations
Overlay Zones
Character, Historic, View Protections
Context
Incentives
Zoning
Residential
Mixed-use
Non-residential
Edge buffers
Centers & Corridors
Small-area & Area of Consistency rules
Distance separations
Proximity to residential
Planned Development
Development types
Uses
Building design standards
Edge buffers
IDO Zoning Map
https://tinyurl.com/IDOzoningmap
1-8
Hierarchy of Rules
https://abq-zone.com
Notes: Improved description of how rules are applied in Part 1. (Section 14-16-1-8)
Any update to improve quality standard citywide WON’T apply to tailored standard. (Sometimes that’s good, sometimes that’s not. Need to review carefully!)
Tradeoff is additional complexity for extra protections.
Zoning is not easy, but it IS more predictable now under the IDO.

## Slide 8: Tailored Protections
IDO Part 4
Allowable Uses
IDO Part 5
Development Standards
IDO Part 6
Admin & Enforcement
Review
Procedures
Small Area
Standards
Use-
specific
Standards
IDO Part 3
Overlay Zones
View
Character
Historic
Protection
https://tinyurl.com/IDOzoningmap
Table
I
Table II
Small Area
Indexes
IDO Zoning Map
https://abq-zone.com

## Slide 9: Small Areas
Examples:
Where are drive-thoughs are prohibited in ABQ?
Where are ADUs with kitchens allowed in R-1?
Table I: IDO Order
(for questions throughout the city)
Table II: Alphabetical Order
(for questions about 1 area)
Examples:
What are the special rules near the airport?
What special protections apply to Barelas?

## Slide 10: Implementing Centers & Corridors
DT = Downtown
UC = Urban Center
AC = Activity Center
EC = Employment Center
MS = 660 feet from Main Street
PT = 660 feet from Premium Transit station
MT = 660 feet from Major Transit
Center/Corridor
Index
Table III
https://tinyurl.com/IDOzoningmap
IDO Zoning Map
UC
DT
AC
EC
MT
MS
https://abq-zone.com

## Slide 11: Major Public Open Space Edges
Single-loaded road required
  45 feet minimum OR landscaped buffer
Rules apply adjacent to MPOS
  Exception if separated by principal arterial or freeway (in which case w/in 330 feet rules apply)
  Existing vegetation can count toward landscape requirement
  For cluster development and multi-family, required to locate 25% of common open space or ground-level usable open space contiguous with MPOS
Section 5-2(J)
https://tinyurl.com/IDOzoningmap
IDO Zoning Map
ido.abc-zone.com

## Slide 12: Zoning
https://tinyurl.com/IDOzoningmap
Residential
Zone Districts
Mixed-use
Zone Districts
Non-residential
Zone Districts
Planned Development
Zone Districts
Unclassified

## Slide 13: overlay zones
https://tinyurl.com/IDOzoningmap
Part 3
ido.abc-zone.com

## Slide 14
IDO Part 4
Allowable Uses
Distance separations from residential and
Open Space areas and between uses
Use-
specific
Standards
https://tinyurl.com/IDOzoningmap
  From Residential Uses: Liquor retail, Heavy Manufacturing, Auto repair, etc.
  From Open Space: Car wash, Gas stations, Manufacturing, Solid Waste, etc.
  Between uses: Group Homes, Pawn Shops, Bail Bonds, Payday Loans, etc.
IDO Zoning Map
https://abq-zone.com
Notes:   Between uses: Group Homes, Pawn Shops, Bail Bonds, Payday Loans, etc.
  From Residential Uses: Retail Liquor, Heavy/Special Manufacturing, Auto repair, etc.

## Slide 15: Use table
Table 4-2-1: Allowable Uses P = Permissive Primary C = Conditional Primary A = Permissive Accessory CA = Conditional Accessory CV = Conditional if Structure Vacant for 5+ years T = Temporary CT = Conditional Temporary Blank Cell = Not Allowed |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Zone District >> Land Uses | Residential |  |  |  |  |  | Mixed-use |  |  |  | Non-residential |  |  |  |  |  |  |  | Use-specific Standards
 | R-A | R-1 | R-MC | R-T | R-ML | R-MH | MX-T | MX-L | MX-M | MX-H | NR-C | NR-BP | NR-LM | NR-GM | NR-SU | NR-PO |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | A | B | C | 
PRIMARY USES THAT MAY BE ACCESSORY IN SOME ZONE DISTRICTS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RESIDENTIAL USES |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Household Living |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Group Living |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CIVIC AND INSTITUTIONAL USES |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
COMMERCIAL USES |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Agriculture and Animal-related |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Food, Beverage, and Indoor Entertainment |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Lodging |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Motor Vehicle-related |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Offices and Services |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Outdoor Recreation and Entertainment |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Retail Sales |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Transportation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
INDUSTRIAL USES |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Manufacturing, Fabrication, and Assembly |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Telecommunications, Towers, and Utilities |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Waste and Recycling |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Wholesaling and Storage |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ACCESSORY AND TEMPORARY USES |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ACCESSORY USES |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TEMPORARY USES |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Table
4-2-1
7-1
Definitions
Notes: Delete USS in bottom of table

## Slide 16
IDO Part 5
Development Standards
Rules that set quality standards for development
Context Rules
Transitions:
Neighborhood Edges, Edge Buffers
Major Public Open Space Edges
https://tinyurl.com/IDOzoningmap
https://abq-zone.com
Notes:   Between uses: Group Homes, Pawn Shops, Bail Bonds, Payday Loans, etc.
  From Residential Uses: Retail Liquor, Heavy/Special Manufacturing, Auto repair, etc.

## Slide 17: Limits on Density
Citywide
Building height
Required usable open space
Required parking
Required landscaping
Building design standards
CONTEXTUAL
Use-specific standards
  Distance from residential
Neighborhood Edges
Edge Buffers
Major Public Open Space Edge
Part 5
Notes: Areas of Change and Consistency for Edge Buffers

## Slide 18: Dimensional Standard Tables: By Zone Categories
Categories
Zones
(By intensity)
Acronyms
Center Provisions
5-1
Notes: Be ready to define terms

## Slide 19: Off-street parking
Table by Allowable Use
Reductions in Centers + Corridors
UC = Urban Center
MS = 660 feet from Main Street
PT = 660 feet from Premium Transit station
https://tinyurl.com/IDOzoningmap
Table 5-5-1
https://abq-zone.com

## Slide 20: Off-street parking
Table by Allowable Use
Reductions for Transit
Reduction | Location or Distance | Peak Service Frequency
50% | Premium Transit (PT) areas | 15 min
30% | Within ¼ mile of stop/station | 15 min
10% | Within 330 feet of stop/station | 45 min
Reduction | Location or Distance | Peak Service Frequency
50% | Premium Transit (PT) areas | 
30% | Within ¼ mile of stop/station | 
10% | Within 330 feet of stop/station | 
Louisiana
University
San Mateo
Broadway
Atrisco
Coors
Unser
https://tinyurl.com/IDOzoningmap
Section 5-5(C)
https://abq-zone.com

## Slide 21: standards
5-1 Dimensional Standards
5-2 Site Design + Sensitive Lands
5-3 Access + Connectivity
5-4 Subdivision of Land
5-5 Parking + Loading
5-6 Landscaping, Buffering, + Screening
5-7 Walls + Fences
5-8 Outdoor + Site Lighting
5-9 Neighborhood Edges
5-10 Solar Access
5-11 Signs
Part 5

## Slide 22: Finding the Balance
Streamlined Approval Process
More administrative review
Community Input
Early consultation
& more public notice
Intent
If we get the rules right – and we need to continually work to get the rules right – and projects follow those rules, they get approved quickly.
Asking for exceptions means more notice, more public input, and a longer process.

## Slide 23: Review/decision
Part 6
https://abq-zone.com
https://compplan-abq-zone.com
Some notice.
Administrative review.
Decided on IDO rules only.
Neighborhood Meeting.
More notice.
Public meeting or hearing.
Decided on IDO rules only.
Neighborhood Meeting.
Lots of notice.
Public hearing.
Rules decided case-by-case.
Comp Plan policies AND IDO regulations apply.
Table 6-1-1
Notes: Find chart. Make handout.

## Slide 24
Part 6
Finding the balance
Predictability
Flexibility
Discretionary Decisions:
Public Hearing
Pre-application Neighborhood Meeting required
Lots of notice required
Rules decided case-by-case (Comp Plan applies)
Early Stage / Projects requesting exceptions:
Public Hearing
Pre-application Tribal Meeting required
Lots of notice required
Rules decided annually during IDO Update
Last Stage / Projects following rules:
Administrative decision
Some notice required
Rules decided annually during IDO update
Administrative Decisions
Decisions
Requiring a Public Hearing
Policy Decisions
Notes: Handout

## Slide 25
Table 6-1-1

## Slide 26
Resources
Planning Webpage
compplan.abq-zone.com
ABC Comp Plan
cabq.gov/planning
abq-zone.com
Interactive IDO
tinyurl.com/idozoningmap
IDO Zoning Map
Michael Vos
Principal Planner
mvos@cabq.gov